Product Name： IR 24 Keys WIFI Controller

Product Description:

This mini IR 24-key WIFI controller is a new way to use your Smart lighting system。As a member of the series, it is manipulated by connect to wireless router. This is designed to make using your smart lighting system much easier and more convenient. No matter where you are, when it is, you can always control them. Functions like 16 million colors, 20 dynamic modes, music, and picture color recognize.

Technical Parameters:

● Working temperature：-20-60℃

● Input voltage：DC5-28V

● Output：3/4 circuit

● Connection mode：Common anode

● controller size：53mm*24mm*11mm

● remote size：L85×W52×H7mm

● Net weight：45g

● Gross weight：50g

● Static power consumption：<0.5W

● Output current：<4A(each circuit)

● Output power： 5V:<60W, 12V:<144W, 24V:<288W（3 circuit）

Direction for use:

- Connect the load wire at first, following by the power wire; Please ensure short circuit can not occur between connecting wire before you turn on the power；

- The key functions are as below:

| Symbol | Key note | Symbol | Key note | Symbol | Key note | Symbol | Key note |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Brightness + |  | Brightness- |  | OFF |  | ON |
|  | Static red |  | Static green |  | Static blue |  | Static white |
|  | Static orange |  | Static pea green |  | Static dark blue |  | Strobe flash |
|  | Static dark yellow |  | Static cyan |  | Static brown |  | 7 color jump change |
|  | Static yellow |  | Static light blue |  | Static pink |  | 7 color fade change |
|  | Static straw yellow |  | Static sky blue |  | Static purple |  | 3 color jump |

Steps for reorder the sequencing:

1、If you want to change the output channel, the steps are as follows: repower the controller on; when the press the key G for 2 to 3s,the light flashes, long flickering white light

means you've successfully change the output channel to GRB; Similarly, long press key B

change the channel to BGR, will sequence; long press key R to RGB sequence.

2、In the RGBW version, press W key for RGB and white light; long press W key for 2 seconds will switch to W channel.

Product Features:

- Support for 16 million kinds of color and

Brightness adjustment control
2.Channel:RGB,'RGBW,

3.Support for color and dynamic mode

Customization and preservation
4.Group synchronization control function
5.The switch time, static ,and dynamic display of

the light can be set
6.Lights and music sync functions
7.A variety of built-in dynamic model, and the

custom dynamic model

8.Remote control function
9.The microphone sound control function
10.The camera takes the background color and the
setting of the scene

Mobile APP installation instructions:

1.Product software APP name: Magic Home Pro
a. Apple users can search "Magic Home Pro” in "APP
Store"; Android users can search "Magic Home Pro"
in "Google Play Store" or from browsers.  The APP is
free to download and use.

b. Scan the QR code below to download and install the APP for free.(Please click“ open the web link from the browser ”when you use Wechat to scan the QR for the Wechat itself has  no browser function.)

Usage description:
1.Please use this product in a dry environment
2.Please use the voltage for dc current of dc5-28v,and not to use 220V alternating  current.
3.The product is a common anode connection.After installed the WIFI controller,open  mobile WIFI network signal, find “LED net*****”signal and connect, open the Magic Home Pro APP ,there are three kinds of connection mode to connect the controller.

The first: choose to connect directly to the controller ;enter the APP control interface.

The second: choose to connect to the router, write the router password , mobile phone choose the to connect the router network signal, open the Magic Home Pro APP, enter the software APP control interface

The third: choose to connect the router and keep the router in a network connection, remote control can be performed

The Android Operating Interface Instructions:
In the use of the APP, please make sure that the
controller circuit and power supply is normal connection. 1.Single connection: do not need to register account,open cell phone WIFI network,find“LED net**”signal and connect.

- Add the controller's signal to the router for connection control.

When registering the account ,please connect the controller's WIFI signal to the router (make sure the network is accessible)

- Remote connection settings
When making remote Settings, make sure the account is logged in properly

The apple operating interface instructions:In the use of the APP,please make sure that the controller circuit and power supply is normal connection
1.Single connection: do not need to register account, open cell phone WIFI network, find“LED net…”signal and connect.

2. Add the controller's signal to the router for connection control.

When registering the account, please connect the controller's WIFI signal to the

router(make sure the network is accessible)

Note: if you want to add controller WIFI to the router network in the APP interface, you should connect the controller signal in network connection first.

3.Remote connection settings.

When making remote settings，make sure the account is logged in properly

Step 1: Create your Magic Home cloud account

In order to control your smart light with the Amazon Echo or control them remotely, youneed to create a MagicHome cloud accountand sign in.

Step 2:Add your light and modify the name

Make sure there is at least one smart lightin device list, and enable your lights for remotecontrol. On "Home" page,long press lighttorename.

Step 3: EnableAlexa Skill

The next step is to download the Amazon Alexa app , open the Amazon Alexa app andunder the skills section, search for the Magic Home skill. The account and passwordmust be same as you created in Magic Home Pro APP.

Step 4: Login and Discover Devices

Useyour MagicHome cloud account you created in step 1 to signin to "Magic Home" Skill.The next step is to discover your smart lightsfrom Alexa app. You can say Alexa, discoverdevices

Once Alexa has comp leted discovering your smart lights, they will be shownin the SmartHome section in Alexa app.

Step 5: Control your light

Here, you finish all setups. You can now control your lights by issuing voice commands.Supported Commands:

These are some of the currently supported Alexa voice commands for the smart light.Alexa, set [light name] to [0-l00]%Alexa, turn [light name] on/offAlexa, dim/brighten [light name]

Alexa, increase/decrease [light name]Alexa, set the [light name] light to red

Alexa, change the [light name] to the color blueAlexa, make the [light name] warm white

Alexa, change the [light name] to the cool whiteAlexa, set the [light name] to daylightChanging colors on your lights

Color Options for Alexa control of your smart device:o

Blue  Orange  Crimson  Pink  Cyan  Purple  Fuchsia  Red

Gold  Salmon  Green  Sky  Blue  Lavender  Teal

Lime  Turquoise  Magenta  Violet  Yellow

Step 1: Create your Magic Home cloud account

In order to control your smart light with the Amazon Echo or control them remotely, youneed to create a MagicHome cloud accountand sign in.

Step 2:Add your light and modify the name

Make sure there is at least one smart lightin device list, and enable your lights for remotecontrol. On "Home" page,long press lighttorename.

Step 3: Add Home Control Action

Click Home control on Home APP. Select Magic Home WiFi" The account andpassword must be same as the one you created in Magic HomeProAPP.

Step4: Login with your app account

Enter your app account and password to finish the account linking. (Use the Magic Homecloud account you used on step 1). Your lights will belisted on Home Control interface.

Step 5: Control your light

Here, you finish all setups. You can now control your lights by issuing voice commands.Supported Commands:

Say "Ok Google" or "Hey Google", then...Turn on <light name>Dim <light name>

Brighten <light name>Set <light name> to [50%]

Dim/Brighten <light name> by [50%]Turn <light name> [color]Turn on/off all thelightsIs <light name> on?

Changing colors on your lights

Color Options for Google Home control of your smart device:

Blue  Orange  Crimson  Purple  Cyan  Red  Fuchsia  Salmon  Gold  Sky Blue   Green  Teal

Lavender  Turquoise  Lime  Violet  Magenta  Yellow

Remote control

1. We have maintained long -term cooperation with the US Ali Cloud Terminal

in USAserverto provide our customers with better remote control services.

2. When and only when you register and loginyouraccountin Magic HomeProAPP,No matter where you are, you still can control your home light withAPP as longasthere 's WiFi/2G/3G/4G internetfor your smart phone.

3.Note:After the controller is bound to home WIFI, it will not display on your WIFIlistanymore.

Common Problem Analysis:

1. Why can'tmy smart phonefind the Wi-Fi signalofcontroller?

Please check ifthe controller has been connected with router or not, atthe sametime the Wi-Fifunction of phone works properly.2. Whycan'tthe controller connect with router?

Firstly, please ensure to input the correct Wi-Fipassword.

Ifthe password iscorrectand the controller stillfails to connect with router,please shutdown the controller and router, then turn on the router and thecontroller 30 seconds later. And waitfor 2 minutes before you starttheAPP.

Ifthe problem cannot solved after the above operations, please restore factorydefaults.

3. Why doesn'tthe controller show in the APP after choose the Wi-Fi signal of the

controllerinthe phone setting?

Please refresh the APP device list by sliding down on the screen. If still not find thecontroller, please try to shutdown the function of smartInternet selection ofyour smartphone settings. This is to avoid automatically exitthe controller signalconnection because of the unavailable network.l. How to resetthe controller?

Reset the WiFi controller by plug and unplug connector repeatly for 4 times, waitfor 1-3seconds each time you plug/unplug the connector. (Please refer to thediagraminAPP HELPS for more details)

Cautions

1, This products Input voltage is DC5-28v, other input voltage are not allowed.

2, Lead wire should be connected correctly, according to the wire color and the connecting diagram offers；

3, Overload are prohibited.